Title
Linux on AMD64
Michal Ludvig
michal@logix.cz
http://www.logix.cz/michal

---
x86 – your 32 bit CPU
No significant changes since 80386 (1985!)
LP32 architecture
  - can address 232 bytes = 4GB per process
  - max 4GB of physical RAM
  - with ugly hacks up to 64GB RAM
    - still only 4GB/task!
each process has its own virtual memory
  - code, libraries, data and kernel share the same address space

---
Going 64 bit – AMD64
LP64 – long int and pointers have 64 bits
  - huge addressable space: 264 Bytes is a lot
  - faster operations with large integers
multiple operating modes
  - backward compatible real and protected modes
  - long mode for native 64 bit kernel and processes
    - 32b processes run in legacy mode under 64bit kernel
      - fast, native, not emulated like on Itanium
[Speaker Notes: Boot up DOS or Windows95]

---
AMD Opteron and Athlon64 (I.)
Improved core architecture
  - 64 bit long mode
  - Doubled number of GPRs
  - Supports 3Dnow!, SSE and SSE2 with 16 XMM/128b registers
  - NX pages against buffer overflows
IOMMU unit
  - gives 32 bit PCI cards access to the whole 64 bit address space

---
AMD Opteron and Athlon64 (II.)
  - integrated memory controller
    - can address L1, L2 cache and main memory at the same time
    - memory attached directly to the CPU
  - multiple HyperTransport buses for connecting CPU↔CPU and CPU↔peripherals
    - up to 12.8 GB/s full duplex

---
Intel EM64T
New Xeons with 800MHz FSB
Instruction-wise compatible with AMD64
Doesn't have integrated memory controller
Doesn't have IOMMU
  - 32 bit PCI cards may slow the system
No HyperTransport – limited to single FSB
SSE3 instead of 3Dnow!

---
MP systems – NUMA vs SMP
NUMA – Non-Uniform Memory Access
  - each CPU has its own memory
  - indirect access to other CPU's memory
SMP – Symmetric Multi-Processing
  - all CPUs access the same memory
  - single memory controller in northbridge
CPU
CPU
NorthBridge
R A M
[Speaker Notes: NUMA is used in SGI Altix systems with Intel Itanium2 CPUs]

---
NUMA + SMP = SUMO
Sufficiently Uniform Memory Organization
  - introduced in AMD64 MP systems
  - each CPU has directly attached memory
  - high speed access to other memory over HyperTransport bus
  - transparent to the operating system
R
A
M
HyperTransport
CPU
CPU
R
A
M

---
Linux on x86-64
kernel is fully ported
  - including all HW drivers, frame buffer, software suspend, power management, ...
  - 64bit kernel supports both 32bit and 64bit tasks
    - e.g. 32 bit Firefox runs just fine in 64 bit X11
most userspace programs run in 64 bits
redesigned ABI for faster run
  - calling conventions enjoy more registers

---
cat /proc/cpuinfo
processor : 0
vendor_id : AuthenticAMD
cpu family : 15
model : 12
model name : AMD Athlon(tm) 64 Processor 3200+
stepping : 0
cpu MHz : 2211.110
cache size : 512 KB
fpu : yes
fpu_exception : yes
cpuid level : 1
wp : yes
flags : fpu vme de pse tsc msr pae mce cx8 apic sep mtrr pge mca cmov pat pse36 clflush mmx fxsr sse sse2 syscall nx mmxext lm 3dnowext 3dnow
bogomips : 4430.14
TLB size : 1024 4K pages
clflush size : 64
cache_alignment : 64
address sizes : 40 bits physical, 48 bits virtual
power management: ts fid vid ttp

---
Applications
System provides both 32 bit and 64 bit libs
32 bit system:
x86:~$ file /bin/echo
/bin/echo: ELF 32-bit LSB executable, Intel 80386, version 1 (SYSV), [...]
x86:~$ ldd /bin/echo
libc.so.6 => /lib/tls/libc.so.6 (0x4002e000)
/lib/ld-linux.so.2 => /lib/ld-linux.so.2 (0x40000000)
64 bit system:
x86-64:~ $ file /bin/echo
/bin/echo: ELF 64-bit LSB executable, AMD x86-64, version 1 (SYSV), [...]
x86-64:~$ ldd /bin/echo
libc.so.6 => /lib64/tls/libc.so.6 (0x00002aaaaabc2000)
/lib64/ld-linux-x86-64.so.2 => /lib64/ld-linux-x86-64.so.2
(0x00002aaaaaaab000)

---
Low level
  - extended registers: AL→AX→EAX→RAX
  - extra eight registers called R8 to R15
  - GCC can generate both 64 bit and 32 bit code
    - default is 64 bit code
    - gcc -m32 for 32 bit output

---
Instruction set
System calls via syscall
  - no int 0x80 anymore
Extended AT&T assembly syntax
    - movl	$1, %eax	; 32 bits
    - movq	$1, %rax	; 64 bits
RIP-relative addressing
    - movl	$1, symbol(%rip)
REX prefix

---
Distributions
ported by SUSE
all patches given back to community
installation and look&feel is the same as on x86
most major distributions have AMD64/x86-64 variant
SUSE still actively develops AMD64 kernel and toolchain
  - at least the kernel and GCC for AMD64 are a step ahead of other distributions

---
Porting Linux to AMD64 (I.)
Close cooperation between SUSE and AMD
  - some CPU features requested by SUSE hackers
  - direct contact without the managers' overhead
  - famous dinners paid by AMD ;-)

---
Porting Linux to AMD64 (II.)
mostly done on simulators (Virtutech Simics)
toolchain development heavily used cross compilation
core porting – ca 10 developers in 2 years
  - binutils, GCC, kernel, glibc, GDB
remaining >2000 packages was much easier task
[Speaker Notes: Common problems: - va_list - x86 asm routines - improper stack operations - legal code on the stack collides with NX]

---
Porting Linux to AMD64 (III.)
first real Claw hammer CPU in SUSE
  - 800MHz
  - disabled caches and TLB
  - really slow but still much faster than Simics
  - motherboard Solo
the only other AMD64 system outside AMD was in Microsoft
[Speaker Notes: TLB – translation lookaside buffer MP system - motherboard Melody - CPU board Percussion]

---
Useful links
AMD64 developers guide (5 volumes)
AMD64 Application Binary Interface
Gentle Introduction to x86-64 Assembly
AMD64 registers overview

---
Thank you